## Slide 1: Quality Planning

## Slide 2: Quality Planning
Definition
Grade
Statistics
  Control limits
  Normal Distribution
  Standard deviation
Quality Planning Tools
  Measurement terminology
    Tolerances
  Defining and meeting client expectations
Quality Assurance

## Slide 3: Before we start
During my, Ziko, HP orientation in late 1984, someone said:
  “You can’t manage what you don’t measure” and it stuck to my head.
  What does the above statement mean?
I have also heard quality experts say:
  If you can’t measure it, you can’t improve it!

## Slide 4: Definition of Quality
PMBOK Guide V.5:
  "Quality - The degree to which a set of inherent characteristics fulfills requirements.
Conformance to requirements: The project’s processes and products meet written specifications
Fitness for use: A product can be used as it was intended

## Slide 5: Cost of Quality
The cost of quality is the cost of conformance plus the cost of nonconformance:
  Cost of Conformance means delivering products that meet requirements and fitness for use
  Cost of nonconformance means taking responsibility for failures or not meeting quality expectations

## Slide 6: Grades as a measure of quality
Pre-set standards
  Octane rating for gasoline
  Horsepower in cars
  Lumber graded for appearance, strength
  Steel and other commodities

## Slide 7: Using statistics to measure and manage quality
Control limits
  Upper and lower standards for allowable variation
Central limit theorem
  Frequency distribution
  Discrete math— “bins” –count the number of measurements that fall in each bin
  Normal distribution– “bell-shaped curve”

## Slide 8: Measuring your products
Options:
  Measure entire population:
    When does this make sense?
  Sampling
    Smaller amount of data to work with:
      What is the appropriate percentage?
    Sometimes measuring destroys the sample:
      Destructive testing

## Slide 9: Normal Distribution
Figure 18.2.2 One Sigma Range
Source: http://pm4id.org/10/1/

## Slide 10: Normal Distribution
Standard deviation
  Calculate the mean (or average value) of all measurements
  Subtract EACH measurement from the mean
  Square EACH difference
  Sum the values
  Divide the sum by ( (number of values) – 1 )
  Take the square root
Result can be thought of as the average difference

## Slide 11: The 68-95-99.7 Rule
Figure 18.2.3 The 68-95-99.7 Rule
Source: http://pm4id.org/10/1/

## Slide 12: Sigma Levels
Figure 18.2.4 Meaning of Sigma Levels
Source: http://pm4id.org/10/1/

## Slide 13: Quality Plan
The quality plan specifies the control limits
Often written as the mean ± the acceptable variation
The size of the range is called the tolerance
May specify material to be used
May include people training
May include quality tools

## Slide 14: Quality Assurance (QA)
A program for the systematic monitoring and evaluation of the various aspects of a project, service, or facility to ensure that standards of quality are being met:
  Benchmarking: Comparing your product/service/process quality to key competitors
  Quality Audit: is the process of systematic examination of a quality system carried out by an internal or external quality auditor or an audit team

## Slide 15: Quality Control (QC)
An aggregate of activities (such as design analysis and inspection for defects) designed to ensure adequate quality especially in manufactured products:
  Acceptance decisions
  Rework
  Process adjustments

## Slide 16: Quality planning techniques
Cost-benefit analysis
Benchmarking
Experimentation design
Control Charts
Cause and Effect diagrams
Pareto diagram
Flow charts

## Slide 17: Control Charts (SPC)

## Slide 18: Cause-and-Effect Diagram (aka fishbone diagram)

## Slide 19: Pareto Chart

## Slide 20: Flow Chart (traditional)

## Slide 21: Flow Chart (swim lanes)

## Slide 22: TQC/TQM (never ending cycle)

## Slide 23: Quality Responsibility
Who is most responsible for quality on a project:
  Sponsor?
  PM?
  Team members?
Who is most responsible for quality in a Company:
  CEO?
  PMs?
  Employees?

## Slide 24: Summary
Purpose of Quality Management:
  Build confidence in clients that quality standards and procedures are being followed
Ensured by
  Internal review of plan
  Testing
  Revising policies
  External Review or audit

## Slide 25: Questions?